## Slide 1: Cache Exercises, Virtual Memory

## Slide 2: Exercise 1
What is the total number of reads?
What is the total number of reads that miss in the cache?
What is the miss rate?
Will increasing the Cache size improve the performance?
Will increasing the Block size improve performance?

## Slide 3: Visualize the Cache and Main Memory
… … … … …
Block 63, 127
grid[0][0] | grid[0][1]
grid[0][2] | grid[0][3]
grid[0][4] | grid[0][5]
… … | 
grid[8][0] | grid[8][1]
… | 
grid[15][14] | grid[15][15]
… … | 
Block 0, 64
Block 1, 65
Block 2, 66
Cache
0
1
2
..
..
..
63
16 B
Main Memory
0
1
2
…
64
…
127
16 B
Sequence of accesses
//1st nested for sequence
grid[0][0] -> miss
grid[0][1] -> hit
…
grid[8][0] -> miss
grid[8][1] -> hit
…
grid[15][14] -> miss
grid[15][15] -> hit
//2nd nested for sequence
grid[0][0] -> miss
grid[0][1] -> hit
…
grid[15][0] -> miss
grid[15][1] -> hit
50% MISS RATE

## Slide 4: If we double the cache
… … … … …
Cache
0
1
2
..
..
..
..
127
Block 0
Block 1
Block 2
16 B
Block 127
Sequence of accesses
//1st nested for sequence
grid[0][0] -> miss
grid[0][1] -> hit
…
grid[8][0] -> miss
grid[8][1] -> hit
…
grid[15][14] -> miss
grid[15][15] -> hit
//2nd nested for sequence
grid[0][0] -> hit
grid[0][1] -> hit
…
grid[8][0] -> hit
grid[8][1] -> hit
…
grid[15][0] -> hit
grid[15][1] -> hit
25% MISS RATE

## Slide 5
What is the total number of reads?
  512
What is the total number of reads that miss in the cache?
  256
What is the miss rate?
  50%
Will doubling the Cache size improve the performance?
  Yes
  What will the number of misses in this case?
    128 misses for the first nested for loop sequence. 0 misses for the next nested for loop sequence.
Will increasing the Block size improve performance?
  Yes

## Slide 6: Exercise 2

## Slide 7: Visualize the Cache and Main Memory
Sequence of accesses
grid[0][0] -> miss
grid[0][0] -> hit
grid[1][0] -> miss
grid[1][0] -> hit
…
grid[8][0] -> miss
grid[8][0] -> hit
…
grid[15][0] -> miss
grid[15][0] -> hit
grid[0][1] -> miss
grid[0][1] -> hit
…
grid[15][1] ->miss
grid[15][1] -> hit
…
grid[0][0] | grid[0][1]
grid[0][2] | grid[0][3]
grid[0][4] | grid[0][5]
… … | 
grid[8][0] | grid[8][1]
… | 
grid[15][14] | grid[15][15]
… … | 
Main Memory
0
1
2
…
64
…
127
16 B
… … … … …
Block 63, 127
Block 0, 64
Block 1, 65
Block 2, 66
Cache
0
1
2
..
..
..
63
16 B

## Slide 8: If we double the cache
… … … … …
Cache
0
1
2
..
..
..
..
127
Block 0
Block 1
Block 2
16 B
Block 127
Sequence of accesses
grid[0][0] -> miss
grid[0][0] -> hit
grid[1][0] -> miss
grid[1][0] -> hit
…
grid[8][0] -> miss
grid[8][0] -> hit
…
grid[15][0] -> miss
grid[15][0] -> hit
grid[0][1] -> hit
grid[0][1] -> hit
…
grid[15][1] -> hit
grid[15][1] -> hit
grid [0][2] -> miss
grid [0][2] -> hit
…
grid[0][3] -> hit
grid[0][3] -> hit
…
25% MISS RATE

## Slide 9: Exercise 2 - Answers
512
256
50%
25%

## Slide 10: Exercise 3 – Try to solve it
Sequence of accesses
grid[0][0]
grid[0][0]
grid[0][1]
grid[0][1]
…
grid[15][14]
grid[15][14]
grid[15][15]
grid[15][15]

## Slide 11: Exercise 3 – Answers
512
128
25%
No

## Slide 12: Virtual Memory

## Slide 14: Consider a Scenario
Main Memory
  Size of Main Memory = 64 Bytes
  Frame Size = 4 Bytes
  Number of Frames = 64/4 = 16
Process
  Size of Process = 16 Bytes
  Page Size = 4 Bytes
  Number of Pages = 16/4 = 4

## Slide 15: Paging
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
B16 | B17 | B18 | B19
B20 | B21 | B22 | B23
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
Process P1
Page 0
Page 1
Page 2
Page 3
Frame 0
Frame 1
Frame 2
Frame 3
Frame 14
Frame 15
Main Memory
Frame 4
Frame 5
Process P1
CPU
VA of B6
= 0110
MMU
PA of B14
How does the MMU get the Physical address of B14 in Main Memory?!!

## Slide 16
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
B16 | B17 | B18 | B19
B20 | B21 | B22 | B23
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Frame 0
Frame 1
Frame 2
Frame 3
Frame 14
Frame 15
Main Memory
Frame 4
Frame 5
Process P1
Frame 2
Frame 3
Frame 4
Frame 5
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
Process P1
Page 0
Page 1
Page 2
Page 3
Page Table of Process P1
Page 0
Page 1
Page 2
Page 3
VA of B6
= 0110
MMU
PA of B14
CPU
How many bits is the Physical Address?
= 001110

## Slide 17: Related Links
You can refer to the following links to know more about virtual memory, how frames are allocated to processes and about the page replacement policies.
  Allocation of frames in Operating Systems
  Page Replacement Algorithms in Operating Systems
  Virtual Memory

## Slide 18: Some Important Byte Conversions
Example:

## Slide 19: Exercise
Physical Address Space (PAS)
  Size of Main Memory
Virtual Address Space (VAS)
  Size of the process
PAS = 128 KB
VAS = 128 KB
How many bits for PA?
  17
How many bits for VA?
  17

## Slide 20: Exercise
Physical Address Space (PAS)
  Size of Main Memory
Virtual Address Space (VAS)
  Size of the process
PAS = 128 KB
VAS = 128 KB
Page Size = 4 KB
How many bits for the page offset?
  12 bits

## Slide 21: Exercise
Physical Address Space (PAS)
  Size of Main Memory
Virtual Address Space (VAS)
  Size of the process
PAS = 128 KB
VAS = 128 KB
Page Size = 4 KB
How many bits for the page number?
  (17 – 12) bits = 5 bits
How many Pages?
  = 32

## Slide 22: Exercise
Physical Address Space (PAS)
  Size of Main Memory
Virtual Address Space (VAS)
  Size of the process
PAS = 128 KB
VAS = 128 KB
Page Size = 4 KB
How many bits for the Frame number?
  (17 – 12) bits = 5 bits
How many Frames?
  = 32

## Slide 23: Exercise
Physical Address Space (PAS)
  Size of Main Memory
Virtual Address Space (VAS)
  Size of the process
PAS = 128 KB
VAS = 128 KB
Page Size = 4 KB
How many bits for a Page Table Entry (PTE)?
  5 bits
*For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 24: Exercise
Physical Address Space (PAS)
  Size of Main Memory
Virtual Address Space (VAS)
  Size of the process
PAS = 128 KB
VAS = 128 KB
Page Size = 4 KB
What is the Size of the Page Table?
  (Number of Pages * Size of a Page Table Entry) = bits
*For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 25: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Physical Pages(or frames) | PTE$ | Size of Page Table
1 MB |  |  |  |  | 10 |  | 256 |  | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 26: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of virtual Pages | # of Physical Pages (or Frames) | PTE$ | Size of Page Table
1 MB |  |  |  |  | 10 |  | 256 |  | 
VAS | PAS | VA | PA | Page Size | Page Offset | # of virtual Pages | # of Physical Pages (or Frames) | PTE$ | Size of Page Table
1 MB |  |  |  |  | 10 |  | 256 |  | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 27: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB | # of Frames * Frame Size = 256 KB |  |  |  | 10 |  | 256 |  | 
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB | # of Frames * Frame Size = 256 KB |  |  |  | 10 |  | 256 |  | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 28: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 |  | 
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 |  | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 29: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 |  | 
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 |  | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 30: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 = 2^8 | 8 bits | 
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 = 2^8 | 8 bits | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 31: Exercise 2
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 = 2^8 | 8 bits | bits
VAS | PAS | VA | PA | Page Size | Page Offset | # of Virtual Pages | # of Frames | PTE$ | Size of Page Table
1 MB = 2^20 Bytes | # of Frames * Frame Size = 256 KB =2^18 Bytes | 20 bits | 18 bits |  | 10 |  | 256 = 2^8 | 8 bits | 
$For this example, we assume that a page table entry contains only the bits to represent the Frame Number.

## Slide 32: TLB

## Slide 33
VPN | PO
Virtual Address
MMU
VPN
PTE
PTE
PTE
.. ..
Page Table
VPN 1
VPN 2
VPN 3
…
…
PPN
Main Memory/Cache
PPN | PO
Physical Address

## Slide 36
PTE
PTE
PTE
PTE
…
…
…
Valid Bit
Tag
0
1
2
3
…
Set 0
Set 1
TLB Tag | TLB Index | PO
Virtual Address
MMU
VPN
2-way set associative TLB
TLB Index, Tag
PPN
PPN | PO
Physical Address
TLB HIT!!

## Slide 40: Cache Tutorial

## Slide 52: References
https://www.youtube.com/watch?v=2i2N_Qo_FyM&list=PLEbnTDJUr_If_BnzJkkN_J0Tl3iXTL8vq
https://www.geeksforgeeks.org/multilevel-paging-in-operating-system/
https://ravindrababuravula.com/index.php