## Slide 1: Cache Memory

## Slide 2: From what we know until now
CPU
Registers
Main Memory
SLOW!!
Low Bus bandwidth
I Process data
I Store data
Access (read/write) data

## Slide 3: Solution – Cache Memory
CPU
Registers
Main Memory (DRAM)
I Process data
I Store data
CACHE (SRAM)
I Store data too
+ FASTER!!
+ Closer to Processor
– More Expensive
– Smaller Capacity
– SLOWER
– Far from Processor
+ Cheaper
+ Larger Capacity
BOTH SRAM and DRAM are VOLATILE memory, i.e., they require power to maintain stored information

## Slide 5: Looking Inside Cache and Main Memory
Cache
LINE
0
1
2
3
Main Memory
0
1
2
3
4
5
6
7
BLOCK
A collection of Cache Lines is called a Cache SET.

## Slide 6: Looking Inside Cache and Main Memory
Cache
LINE
0
1
2
3
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
B16 | B17 | B18 | B19
B20 | B21 | B22 | B23
B24 | B25 | B26 | B27
B28 | B29 | B30 | B31
Main Memory
0
1
2
3
4
5
6
7
BLOCK
LINE SIZE = BLOCK SIZE

## Slide 7: Accessing Data
Cache
0
1
2
3
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
B16 | B17 | B18 | B19
B20 | B21 | B22 | B23
B24 | B25 | B26 | B27
B28 | B29 | B30 | B31
Main Memory
0
1
2
3
4
5
6
7
CPU
Read Byte B2
Step 1: Search in CACHE
IF B2 exists in Cache
HIT
IF B2 NOT found in Cache
MISS
Proceed to Step 2

## Slide 8: Accessing Data
Cache
0
1
2
3
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
B16 | B17 | B18 | B19
B20 | B21 | B22 | B23
B24 | B25 | B26 | B27
B28 | B29 | B30 | B31
Main Memory
0
1
2
3
4
5
6
7
CPU
Read Byte B2
Step 1: Search in CACHE
IF B2 exists in Cache
HIT
IF B2 NOT found in Cache
MISS
Proceed to Step 2
Step 2: Access Byte B2 from Main Memory
Step 3: Copy the entire Block 0 to the Cache

## Slide 9: Two Important Questions
Why did I copy the entire Block 0 to the cache?
In which Cache Line will I place Block 0?

## Slide 10: Two Important Questions
Why did I copy the entire Block 0 to the cache?
In which Cache Line will I place Block 0?

## Slide 11: Locality
“Tendency of a processor to access the same set of memory locations repetitively over a short period of time.”
Spatial
  If a Byte is accessed now then the Byte next to it is likely be accessed next
  The number of Bytes in a block affects spatial locality
Temporal
  If a Byte is referenced now then the same Byte is likely be referenced again in the future

## Slide 12: Two Important Questions
Why did I copy the entire Block 0 to the cache?
In which Cache Line will I place Block 0?

## Slide 13: Mapping
‘In which line of the cache is one block of the main memory mapped to?’
Cache
0
1
2
3
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
B16 | B17 | B18 | B19
B20 | B21 | B22 | B23
B24 | B25 | B26 | B27
B28 | B29 | B30 | B31
Main Memory
0
1
2
3
4
5
6
7
?

## Slide 14: Types of Mapping
Direct Mapping
Fully Associative Mapping
Set Associative

## Slide 15: Consider a Scenario
BYTE addressable
  Address associated with each Byte
Main Memory
  Total number of Bytes = 64
  Divided into Blocks
    Block Size = 4 Bytes
  How many blocks?
    64/4 = 16 Blocks
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory

## Slide 16: Consider a Scenario
Byte addressable
  Address associated with each Byte
Cache
  Total number of Bytes = 16
  Divided into Sets
  1 Set = 1 Line
    Line Size = 4 Bytes
  How many Lines?
    16/4 = 4 Lines
Cache
Line 0
Line 1
Line2
Line 3

## Slide 17
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Cache
Line 0
Line 1
Line 2
Line 3
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Byte Addressable = Each Byte in Main Memory is identified by an address

## Slide 18
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Cache
Line 0
Line 1
Line 2
Line 3
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Number of Bytes in Main Memory = 64 =
How many addresses?
  64
How many bits per address?
  6-bit address

## Slide 19
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Cache
Line 0
Line 1
Line 2
Line 3
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Access Byte B5 in Main Memory
Byte Address = 000101
Block Number
Block Offset

## Slide 20: Direct Mapping

## Slide 21: Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Mapped in Round Robin manner
Line Number/Index = K mod n
  K = Block Number
  n = Number of lines
1 Set = 1 Line, so Line Number and Set Number are the same

## Slide 22: Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
Block 0/4/8/12
Block 1/5/9/13
Block 2/6/10/14
Block 3/7/11/15
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Mapped in Round Robin manner
Line Number/Index = K mod n
  K = Block Number
  n = Number of lines
1 Set = 1 Line , so Line Number and Set Number are the same

## Slide 23: Direct Mapping – Many to One Mapping
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
0
1
2
3
Main Memory Blocks
Cache Lines

## Slide 24: Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
Block 0/4/8/12
Block 1/5/9/13
Block 2/6/10/14
Block 3/7/11/15
Byte address
b5 | b4 | b3 | b2 | b1 | b0
Block Offset
Set/Line Number
Tag
CPU
Read Byte at Address
Step 1: Search in Cache
If MISS, go to Step 2

## Slide 25: Direct Mapping
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Byte address
b5 | b4 | b3 | b2 | b1 | b0
Block Offset
Block Number
CPU
Read Byte at Address
Step 2: Access From Main Memory

## Slide 26: Direct Mapping
Suppose Line 0 of the cache has Tag ’00’
  What are the addresses of the Bytes present in line 0 of the cache?
Tag = 00
0 | 0 | b3 | b2 | b1 | b0
Tag
Line Number
Block Offset
Cache
Line 0
Line 1
Line 2
Line 3

## Slide 27: Direct Mapping
Suppose Line 0 of the cache has Tag ’00’
  What are the addresses of the Bytes present in line 0 of the cache?
Tag = 00
0 | 0 | 0 | 0 | b1 | b0
Tag
Line Number
Block Offset
Cache
Line 0
Line 1
Line 2
Line 3

## Slide 28: Direct Mapping
Suppose Line 0 of the cache has Tag ’00’
  What are the addresses of the Bytes present in line 0 of the cache?
Tag = 00
0 | 0 | 0 | 0 | b1 | b0
Tag
Line Number
00
01
10
11
Cache
Line 0
Line 1
Line 2
Line 3

## Slide 29: Direct Mapping
Suppose Line 0 of the cache has Tag ’00’
  What are the addresses of the Bytes present in line 0 of the cache?
Cache
Line 0
Line 1
Line 2
Line 3
B0, B1, B2, B3
Main Memory Block Number
00
01
10
11
0 | 0 | 0 | 0 | b1 | b0
B0 | B1 | B2 | B3
B4 | B5 | B6 | B7
B8 | B9 | B10 | B11
B12 | B13 | B14 | B15
… … … |  |  | 
B56 | B57 | B58 | B59
B60 | B61 | B62 | B63
Block 0
Block 1
Block 2
Block 3
Block 14
Block 15
Main Memory
Tag
Cache Line Number
Tag 00

## Slide 30: Sequence of Actions
Cache
Line 0
Line 1
Line 2
Line 3
Tag = 01
Tag = 11
Tag = 10
1
1
0
1
Valid
Bit
Step 1: Go to Line Number 01
Step 2: Check Valid Bit. If Valid Bit = 0, then it’s a MISS. If Valid Bit = 1, go to Step 3
Step 3: If Tag matches, then it’s HIT, or else MISS
1 | 0 | 0 | 1 | 0 | 1
Block Offset
Line Number
Tag
Byte Address
CPU
Read Byte at Address

## Slide 31: Sequence of Actions
Cache
Line 0
Line 1
Line 2
Line 3
Tag = 01
Tag = 11
Tag = 10
1
1
0
1
Valid
Bit
This is a MISS!!
1 | 0 | 0 | 1 | 0 | 1
Block Offset
Line Number
Tag
Byte Address

## Slide 32: Sequence of Actions
Cache
Line 0
Line 1
Line 2
Line 3
Tag = 01
Tag = 10
Tag = 10
1
1
0
1
Valid
Bit
This is a HIT!!
1 | 0 | 0 | 1 | 0 | 1
Block Offset
Line Number
Tag
Byte Address

## Slide 33: Disadvantages of Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
5
Sequence of Block Numbers requested by CPU
5, 4, 8 , 12, 9, 13

## Slide 34: Disadvantages of Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
4
5
Sequence of Block Numbers requested by CPU
5, 4, 8 , 12, 9, 13

## Slide 35: Disadvantages of Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
4 8
5
Sequence of Block Numbers requested by CPU
5, 4, 8 , 12, 9, 13
This results in Conflict MISS!!
Waste of Space!!

## Slide 36: Disadvantages of Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
4 8 12
5
Sequence of Block Numbers requested by CPU
5, 4, 8 , 12, 9, 13
This results in Conflict MISS!!
Waste of Space!!

## Slide 37: Disadvantages of Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
4 8 12
5 9
Sequence of Block Numbers requested by CPU
5, 4, 8 , 12, 9, 13
This results in Conflict MISS!!
Waste of Space!!

## Slide 38: Disadvantages of Direct Mapping
Cache
Line 0
Line 1
Line 2
Line 3
4 8 12
5 9 13
Sequence of Block Numbers requested by CPU
5, 4, 8 , 12, 9, 13
Waste of Space!!
This results in Conflict MISS!!

## Slide 39: Solutions
Fully Associative Mapping
  A Main Memory Block can be mapped to any Cache line.
  Advantages: Better Cache Hit Rate
  Disadvantages
    Slow because the valid bit and tag of every cache line has to be compared.
    Expensive due to the high cost of associative-comparison hardware.

## Slide 40: Solutions
Set Associative Mapping
  Cache lines grouped into sets
  A main memory block is mapped to a set
    Associative Mapping within a set
  Tradeoff between Direct Mapping and Fully Associative Mapping
  Disadvantages
    Can still suffer from conflict miss.
More details in next recitation

## Slide 41: References
https://www.youtube.com/watch?v=VePK5TNgQU8
https://www.youtube.com/watch?v=N_OJn7jdKCc
https://en.wikipedia.org/wiki/Cache_placement_policies
Locality